## Slide 1: Economic Case for Decarbonization Process and model scope / methodology
March 23, 2023

## Slide 2: Agenda
Modelling Process
Analytical Scope
Appendix - Model methodology

## Slide 3
Decarbonization and economic analysis is based on each city’s Climate Action Plan
Nearly zero energy municipal and business buildings
Heat pumps replace conventional heating / AC systems
Refurbishment of roofs, facades, and windows
LED lighting conversion, smart lighting
National government commitment - 74% renewable electricity by 2030
Electrification public transport and freight
Change citizen behavior: reduce travel; promote walking, cycling, sharing
Minimize and reduce organic waste
Improve recycling
Minimization of construction and demolition waste
Increased solar / wind installations
Net Zero Carbon
Waste
Electricity
Buildings & Heating
Transportation

## Slide 4: The Climate City Contract (CCC) documents city net-zero commitments along with the roadmap and strategy for achieving the Climate Action Plan. The Economic Model is an analysis tool to create that forecast for inclusion in the CCC.
Climate Action Plans
Model Analysis Breakdown
Goal is 80% carbon reduction off 2030 BAU case (20% residual can be offset)
Climate City Contracts
Map model results to Climate City Contract.
Manage to Plan
Report on progress
13 decarbonization sub-sectors
Maximize ROI
Asset owners
CAPEX vs OPEX
Benefits incl. co-benefits
Define annual decarbonization and cost as a roadmap for cities.
Incremental Investment Needed / Funding Gaps
Work with city finance to map plan to budget
City Investments / Other Asset Owners
90+% of investments not under city control
Funding gaps: seek out alternate funding and/or adjust plan
Adjust implementation to stay on track to net zero goals
Decarbonization projects and timing
Document incentives and regulations to motivate others to invest
Decarbonization and Economic Modeling Process

## Slide 5: Objectives of decarbonization economic modelling process
Key elements and benefits of the model
Purpose of the city decarbonization tool – what it can be used for by each city
Quantification of city “Business as Usual” scope 1 and 2 emissions* in 2020 and in 2030
City data inputs are used to create year 2020 baseline
Analysis of emission reduction potential from 13 decarbonization sub-sectors aligned with city’s Climate Action Plan
13 decarbonization sub-sectors typically make up 90%+ of city’s Scope 1 and 2 emissions
Quantification of economic case for each sub-sector, including co-benefits
Quantify costs and benefits of climate related initiatives to maximize decarbonization and monetary Return on Investment (ROI)
Understand investments required of different stakeholder groups as the foundation for Investment Planning
Test impact of increasing ambition level for certain targets
Visualize & quantify the wide range of co-benefits from climate action.
Integration tool in strategic decision making to enable data driven way of working
Comparisons across cities to highlight and share best practices
Purpose: Adapt and refine the tool to each city, to enable quantification of the economic case for decarbonization – to build the rationale for ambitious climate action, support strategy and identify priority areas as defined in the Climate City Contract
* And scope 3 for waste disposed of outside of the city

## Slide 6: NZC Economic Model is tool for strategic planning
Mathematical calculations for validation and analysis
133 city-specific data inputs
73 city-specific assumptions for 2030
Model also includes hundreds of non-city-specific data inputs and assumptions
12 formatted tables for CCC
Provided by City

## Slide 7: Agenda
Modelling Process
Analytical Scope
Appendix - Model methodology

## Slide 8: Scope of economic case analysis
Key considerations | Proposed scope | 
CO₂ scope – what emissions to include? | Include scope 1 & 2 emissions in the economic case, as cities can often influence these emission sources Scope 3 emissions are included only for city waste disposed of outside of city borders | 
Decarbonization sub-sectors – which sub-sectors to model? | Quantify economic case for 13 abatement sub-sectors within Transportation, Buildings & Heating, Electricity, and Waste Selection of sub-sectors based on expected impact and possibility for cities to influence | 
Costs & co-benefits – which costs to include and co-benefits to quantify? | Societal perspective on costs and benefits (not limited to city boundaries), net OPEX & CAPEX delta Quantify financial costs/benefits, air quality, noise and road safety | 

## Slide 9: Cities generate a wide range of direct and indirect CO₂e emissions
CO₂ source | Scope 1 | Scope 2 | Scope 3
Transport | Tail-pipe emissions from cars, buses, etc. | Emissions from electricity used in EVs, public transport etc. | Materials emissions from production of vehicles Transportation of fuels
Buildings & energy | Emissions from heat production Emissions from construction machines | Electricity used for direct heating and heat pumps Electricity for appliances and lighting | Material-related emissions, e.g. process emissions from cement production
Waste | Emissions from waste logistics CO₂ from waste incineration Methane from landfills | Electricity used in waste management | Material embedded emissions in waste (e.g. plastic packaging)
Other | Emissions from agriculture (e.g. methane) Emissions from industries located within city boundaries | Electricity used within city boundaries (non-transport, buildings, waste) | Food value chain emissions Other indirect emissions (non-electricity related)
Scope 1 – direct emissions
Emissions occurring within city boundaries
Scope 2 – electricity emissions
Emissions from generation of electricity used within city boundaries
Scope 3 – value chain emissions
Non-electricity indirect emissions, e.g. production of cement to buildings built within city boundaries
City boundaries
Scope 1, 2 & 3 explained
Non-exhaustive

## Slide 10: 13 decarbonization sub-sectors selected based on mitigation potential and cities’ influencing potential
Long-list of CO₂ mitigation sub-sectors for scope 1 & 2 emissions
Most promising feasible sub-sectors which cities can influence
Sub-sectors with high medium term1 CO₂ mitigation potential
Transportation sub-sectors
Buildings & heating sub-sectors
Electricity sub-sectors
Waste sub-sectors
Mitigation potential
Sub-sectors with generally moderate and high CO₂ mitigation potential
Potential needs to be achieved in medium-term
Cities’ influencing potential
Sub-sectors where cities have high influence
Feasibility for city to act on sub-sector
1. Until 2030

## Slide 11: Economic case quantifies carbon abatement and costs for emissions that city can more easily influence
CO₂ source | Scope 1 | Scope 2 | Scope 3
Transport | High –Geographical regulations (e.g. “environmental zones”), however no influence on fuel efficiency | Moderate – City able to promote and invest in local, decentralized renewable electricity production | Low – Limited possibility to influence how vehicles are produced (e.g. low-CO₂ materials), except for vehicles procured by the city itself or contractors
Buildings | High – Investments in low-CO₂ and efficient heating (e.g. district heating) and regulation (e.g. ban on oil-based local heating). | High – Energy-efficiency programs, investments in local renewable electricity production. Low influence on electricity use for lighting/appliances | Moderate/Low – Generally low influence, however cities could influence material choices in buildings in the local planning process or when the city sells properties to contractors
Waste | High – Procurement of low-CO₂ logistics, investments in efficient waste management facilities, increase recycling to reduce incineration and landfill | Moderate – Investments in local renewable electricity production | Moderate/Low – Influence waste management outside of city boundaries. Limited possibility to influence how materials ending up in municipal waste are produced.
Other | Moderate – CO₂ regulations on industries and other sectors, however could lead to industries emigrating the city | Moderate – Investments in local renewable electricity production | Moderate/Low – Food efficiency through information, procurement etc. Other sectors’ indirect emissions generally hard to influence
A city’s possibility to influence greenhouse gas emission sources
CO₂ scope

## Slide 12: When building an economic case for decarbonization, different types of costs and benefits are considered
Underlying principles for costs and benefits
Holistic view, including costs and benefits for citizens, businesses, and city
Both costs and benefits are discounted, NPV 2020-2030/40/50 depending on the cost/benefit
Only co-benefits with reliable & established cost data are quantified in the project
Quantifiable co-benefits
B
Reduction of negative externalities
Generation of positive externalities
Qualitative co-benefits
C
Reduction of negative externalities
Generation of positive externalities
Financial costs and benefits
A
Upfront investments (CAPEX delta)
Net recurring costs (net OPEX delta)
The “traditional” economic case
Social value is clear but unclear monetary value
Co-benefits with established monetary value
Included in quantitative cost-benefit analysis
Not included in economic case

## Slide 13: Financial costs have been quantified for each sub-sector taking a societal perspective
13
Calculated with “total societal cost” approach (depending on literature), e.g. cost of a modal shift to public transport = cost of private cars vs public transport per person
Net CAPEX delta: Difference between investments required to realize sub-sector vs. baseline development
Net OPEX delta: Difference between recurring net costs (including potential savings) required to realize sub-sector vs. maintaining existing system
Assumptions are developed for each sub-sector and confirmed with city
Scope of financial costs and benefits
Upfront Investments
Benefits

## Slide 14: Economic case includes a number of quantifiable co-benefits arising from decarbonization
Economic growth
Health
Inclusivity
Transport |  |  |  |  |  |  |  |  |  | 
Buildings & Energy |  |  |  |  |  |  |  |  |  | 
Waste |  |  |  |  |  |  |  |  |  | 
Quantifiable benefits where reliable monetary interpretations exist in literature
Employment
Time savings
Noise
Well-being
Property value
Air quality
Road safety
Equality
Community assets
Qualitatively evaluated co-benefits
Physical health

## Slide 15: Investments, recurring costs/savings, and co-benefits are assigned to six different types of asset owners / beneficiaries
Citizens |  | ✓ |  | ✓ | ✓ | ✓ | ✓ | ✓ | ✓ | ✓
Businesses |  |  | ✓ |  |  |  |  |  |  | 
Cities | ✓ | ✓ | ✓ | ✓ | ✓ |  |  | ✓ |  | ✓
Healthcare providers |  |  |  | ✓ | ✓ | ✓ | ✓ | ✓ |  | 
Transport operators |  | ✓ | ✓ |  |  |  |  |  |  | 
Utilities |  |  |  |  |  |  |  |  |  | 
Typically, 90+% of investment required will not be under the control of the city, and will need to be made by citizens and businesses. In addition, benefits do not always accrue to the group making the investment.
Economic growth
Health
Inclusivity
Employment
Time savings
Noise
Well-being
Property value
Air quality
Road safety
Equality
Community assets
Physical health
Investments and recurring costs / savings are distributed across all beneficiaries
Distribution of co-benefits across beneficiaries

## Slide 16: Model methodology - overview
Sub-sector specific data
Model the sub-sector over time and impacts on the current system
e.g. adaptation to EVs as S-curve. CO₂, NOx etc. reduced by X g/km electrified
1
Model costs and value of co-benefits
e.g. societal costs of NOx of ~9,000 €/t reduced. Initial investment costs of X M€ y1-5, recurring costs of X €/km electrified
2
Produce outputs
e.g. electrification reduces CO₂ emissions by 2030 by X ktonne, with a positive economic case of X M€
3
City specific inputs
Co-benefits database
Costs database
Simple and pragmatic modelling as a function over time
Use average of 2-3 reliable estimates of co-benefit value. Strive to interview experts for important co-benefits
Model baseline
e.g. X million vehicle kilometers traveled per year, expected increase of X% per year by 2030, increased efficiency of ICEs (EU regulations)
0
NPV
Investments until 2030
Co-benefits linked to investments until 2040/2050
Assumptions for sub-sectors
Sub-sector specific data
Dummy values

## Slide 17: What does the Economic Model do and not do (and do with manual support)?
Economic model mathematical calculations
Reasonableness check to ensure data input accuracy
Non-city-specific data and assumptions based on EU averages and research studies
Key Performance Indicators (KPIs) and annual forecast goals
Mathematical forecast of carbon and costs benefits to align with Climate Action Plan
All numerical tables for the Climate Agreement except those for alternative emissions inventory calculations and sources of funds
Cost of the Climate Action Plan in CAPEX and OPEX
How CAPEX and OPEX costs will be funded (investment plan)
Euro value of co-benefits
Return on investment by sector, sub-sector, and asset owner group
Cost and benefits at the project level for activities making up the Climate Action Plan
Scope 1 and 2 emissions (Scope 3 for Waste only)
Scope 3 emissions and costing (other than for Waste)
Emissions and costing outside of the four main sectors of Transportation, Buildings, Electricity and Waste (e.g. industry)
Direct investments (costs directly associated with each sub-sector)
Indirect investments (costs associated with strategic investments, incentives, awareness campaigns etc. to motivate behavior)
Reporting on KPIs versus original forecast within MEL framework
City data / assumptions input sheet
Placeholder data for each input to check for accuracy and as a default when data is not available
”What-if” analysis
Easy interface so cities can input their own data / assumptions and evaluate results

## Slide 18: Agenda
Modelling Process
Analytical Scope
Appendix - Model methodology

## Slide 19
1.1 Reduced motorized passenger transportation need
Reducing passenger kilometres for cars and public transport
Transportation need (passenger kilometres) for cars, public transport & walking/cycling
Vehicle kilometres of cars, public transport & walking/cycling
A
1.2 Shift to public & non-motorized transport
Reducing share passenger cars, increasing public & active transport
1.3 Increased car pooling
Increasing average number of passengers per car
1.4.1 Electrification of cars
Increasing % of total vehicle kilometres for cars that are electrified
1.4.2 Electrification of buses
Increasing % of total vehicle kilometres for buses that are electrified
PASSENGER TRANSPORT
Overview of modelling methodology
Passenger kilometres
New passenger kilometres
Difference in passenger and vehicle kilometres between ‘baseline’ and ‘decarbonization scenario’ for each sub-sector
Noise, accidents, physical activity
Emissions (CO₂ & air pollutants)
Recurring costs/savings (e.g. fuel)
Up-front investments
Total economic case and CO₂ abatement potential
B
C
D
E
New passenger kilometres
Vehicle kilometres
Main modelling steps
Sub-sectors
Economic case calculated for each sub-sector, in step C-E
The sub-sectors’ impact on kilometres travelled modelled in step A-B

## Slide 20
2.1a Optimized logistics
Reducing total tonne-kilometres driven through route optimisation
Transportation need (tonne-kilometres) for trucks
Vehicle kilometres of trucks
A
FREIGHT TRANSPORT
Overview of modelling methodology
tonne kilometres
New tonne kilometres
Difference in vehicle kilometres between ‘baseline’ and ‘decarbonization scenario’ for each sub-sector
Noise, accidents
Emissions (CO₂ & air pollutants)
Recurring costs/savings (e.g. fuel)
Up-front investments
Total economic case and CO₂ abatement potential
B
C
D
E
Main modelling steps
Sub-sectors
Economic case calculated for each sub-sector, in step C-E
The sub-sectors’ impact on kilometres travelled modelled in step A-B
2.1b Optimized logistics
Reducing total vehicle-kilometres driven through increased utilisation
Vehicle kilometres
New vehicle kilometres
2.2 Electrification of trucks
Increasing % of total vehicle kilometres that are electrified

## Slide 21
Energy usage for heating and hot water in building stock
Total heat demand for fossil and renewable heating (district and local heating)
A
3.1 Building renovations
Decreasing the energy demand for heating and hot water in existing building stock
3.2 New efficient buildings
Decreasing energy demand for heating and hot water in new buildings
BUILDINGS AND HEATING
Overview of modelling methodology
Difference in energy usage and production between ‘baseline’ and ‘decarbonization scenario’ for each sub-sector
Emissions (CO₂ & air pollutants)
Recurring costs/savings
Up-front investments
Total economic case and CO₂ abatement potential
B
C
D
E
Main modelling steps
Sub-sectors
Economic case calculated for each sub-sectors, in step C-E
The sub-sectors’ impact on energy usage and production
modelled in step A-B
3.4 Decarbonized heating
Shifting towards renewable sources
Energy demand
Energy demand
Energy demand
New
energy demand
3.3 Efficient lighting & appliances
Decreasing the energy demand for electricity in new and renovated buildings

## Slide 22
4.1 Decarbonizing electricity
Increasing share of renewable electricity generation
Total electricity demand in the city per source of production (including increased electricity demand from other sub-sectors)
A
ELECTRICITY
Overview of modelling methodology
Electricity demand (TWh)
Difference in share of renewable energy between ‘baseline’ and ‘decarbonization scenario’.
Emissions (CO₂ & air pollutants)
Recurring costs/
revenues
Up-front investments
Total economic case and CO₂ abatement potential
C
D
E
Main modelling steps
Sub-sectors
Economic case calculated for each sub-sector, in step C-E
The sub-sectors’ impact on electricity production modelled in step A-B

## Slide 23
5.1 Increased waste recycling
Reducing tonne waste treated at incineration and landfill stations
Total amount of collected waste
Total amount of waste in landfill, incineration, or sorting facilities
A
WASTE MANAGEMENT
Overview of modelling methodology
Tonnes waste collected
Tonnes waste sent to landfill, incineration, or sorting for recycling
B
Main modelling steps
Sub-sectors
The sub-sectors’ impact on waste management modelled in step A-B
Difference in share of waste landfilled, incinerated, and sorted for recycling between ‘baseline’ and ‘decarbonization scenario’.
Emissions (CO₂ & air pollutants)
Recurring costs/
revenues
Up-front investments
Total economic case and CO₂ abatement potential
C
D
E
Economic case calculated for each sub-sectors, in step C-E